Hanover Township

(Beaver County, Pennsylvania)

Subdivision and Land Development

Ordinance #56

12 April 2010

Hanover Township

Subdivision and Land Development Ordinance

Township Supervisors

Gregory Deluca, Chairman

David Morgan, Vice Chairman

Samuel Minich

Planning Commission

John McNary, Chairman

Les Brown, Vice Chairman

John Hudack, Secretary/Coordinator

Jim Buchanan

Leonard Osterling

Zoning Hearing Board

Roger McCarrell, Chairman

Martin Hozak

Steve Zalusky

Phillip Read, Zoning Officer

Widmer Engineering, Inc.

John L. Butya, Solicitor

This project was financed, in part, by a grant from the Commonwealth of Pennsylvania, Department of Community and Economic Development, Land Use Planning

and Technical Assistance Program.

Table of Contents

Page Number

Article I, General Provisions

Section 101 Short Title	1

Section 102 Purpose	1

Section 103 Authority	1

Section 104 Jurisdiction	1

Section 105 Municipal Responsibility and Liability	2

Section 106 Types of Subdivisions and Land Developments Governed by This Ordinance	2

Section 107 Legal Standing	2

Section 108 Unlawful Recording or Sale of Lots	3

Section 109 Effective Date and Repealer	3

Section 110 Subdivision Administrator	3

Section 111 Recording	3

Article II, Definitions

Section 201 General Interpretations	4

Section 202 Meaning of Words	4

Article III, Procedures – Major Subdivisions, Minor Subdivisions, Mobile Home Parks, and

Land Developments

Section 301 Introduction	10

Section 302 Procedures for Major Subdivisions, Minor Subdivisions, Lot Line Revisions,

Mobile Home Parks, and Land Developments	10

Section 303 Determination of Minor Subdivisions and Lot Line Revisions	10

Section 304 Approving Body	11

Section 305 Fees	11

Section 306 Sketch Plans/Pre-Submission Conference	11

Section 307 Submission of Plans	11

Section 308 Recording of Plan	13

Article IV, Plan Requirement

Section 401 Sketch Plan	14

Section 402 Preliminary Plan	14

Section 403 Final Plan	17

Section 404 Additional Requirements	19

Article V, Design Standards

Section 501 General	20

Section 502 Streets	21

Section 503 Curbs and Sidewalks	25

Section 504 Blocks	25

Section 505 Lots and Building Lines	26

Section 506 Lot Grading for Subdivisions and Land Developments	26

Section 507 Easements	27

Section 508 Street Names	27

Section 509 Stormwater Drainage	27

Section 510 Utility Regulations for Subdivision and Land Development	27

Section 511 Floodplain Area Regulations	27

Section 512 Sanitary Sewer Systems	28

Section 513 Water Systems	28

Section 514 Landscaping and Street Trees	28

Article VI, Requirement Improvements

Section 601 General	29

Section 602 Improvements	29

Section 603 Monuments and Markers	29

Section 604 Water Supply	30

Section 605 Sanitary Sewage Conveyance	30

Section 606 Storm Sewers	31

Section 607 Streets, Cul-De-Sacs, Curbs, and Sidewalks	31

Section 608 Utilities	32

Section 609 Erosion Control	32

Article VII, Mobile Home Park Regulations

Section 701 Applicability	33

Section 702 Plan Requirements	33

Section 703 Preliminary Plan	33

Section 704 Final Plan Approval	33

Section 705 Design Requirements	34

Section 706 Utility Requirements	36

Article VIII, Land Development Standards

Section 801 Jurisdiction	37

Section 802 Procedures for Land Development (Site Plan)	37

Section 803 Final Plan Review	38

Section 804 Design Standards for Land Developments	38

Section 805 Assurance for Completion and Maintenance of Improvements	40

Section 806 Additional Criteria for Multi-Family Dwellings	40

Article IX, Acceptance of Public Improvements

Section 901 General	41

Article X, Assurances of Completion

Section 1001 General	42

Section 1002 Improvements	42

Section 1003 Financial Security	43

Article XI, Administration, Amendment, and Modification

Section 1101 Amendments	45

Section 1102 Filing Fee and Review	45

Section 1103 Records	45

Section 1104 Appeals	45

Section 1105 Validity 	45

Section 1106 Remedies and Enforcement	45

Section 1107 Modification of Regulations	47

Section 1108 Conflict	47

Article 1

General Provisions

Section 101 Short Title

This Ordinance shall be known as the “Hanover Township, Beaver County, Pennsylvania, Subdivision and Land Development Ordinance.”

Section 102 Purpose

This Ordinance is adopted to help protect and promote the health, safety, and general welfare of the residents of the Township and for the following additional purposes:

102.1	To assure sites suitable for building purposes and human habitation.

102.2	To provide for harmonious, orderly, efficient and integrated development of Hanover Township.

102.3	To assure new development will be coordinated with existing Township development.

102.4	To provide for adequate easements and rights-of-way for drainage and utilities.

102.5	To accommodate prospective traffic, facilitate fire protection and make such provisions as are necessary for public safety and convenience.

102.6	To make provisions for appropriate standards for streets, storm, sanitary sewers, water facilities, curbs, gutters, and such other improvements as shall be considered needed by the Township.

102.7	To promote the sound layout and design for subdivisions and land developments.

102.8	To secure equitable handling of all subdivision plans by providing uniform procedures and standards.

102.9	To implement the Hanover Township Comprehensive Plan.

Section 103 Authority

The Township of Hanover is vested by law with the jurisdiction and control of the subdivision of land, mobile home parks and land development located within the Township in accordance with the powers granted by Article V of the Pennsylvania Municipalities Planning Code. In this Ordinance, required submissions will first be reviewed by the Township Planning Commission; the power to approve or deny rests with the Board of Township Supervisors.

Section 104 Jurisdiction

Plans for subdivisions, mobile home parks and land development within the Township shall be submitted to, and approved by, the Township before they may be recorded. Such approval is in addition to, and does not supersede, those required by other ordinances, resolutions, or regulations of the Township. Developers should also refer to the Township of Hanover Zoning Ordinance, Floodplain Regulations, as well as other Township or County development regulations. Please note, that the description by metes and bounds in the instrument of property transfer does not exempt the seller or transferor from these regulations. [See 515.1(a) of the Pennsylvania Municipalities Planning Code.]

Section 105 Municipal Responsibility and Liability

The provisions within this Ordinance are designed to fulfill the purposes cited in Section 102. The degree of protection sought by the conditions and requirements of this Ordinance for the present and future residents and land owners in the Township is considered reasonable for regulatory purposes. This Ordinance does not imply that compliance with the minimum requirements for subdivisions, mobile home parks, or land developments will render such subdivision, mobile home parks, or land development free from inconveniences, conflicts, danger, or damages. Therefore, this Ordinance shall not create liability on the part of the individual members of the Board of Supervisors, the Township of Hanover Planning Commission, or any officer, appointee, or employee of Hanover Township for any damages that may result from reliance on this Ordinance or any administrative decision lawfully made thereunder.

Section 106 Types of Subdivisions and Land Developments Governed by This Ordinance

106.1	Minor Subdivision: The division of any lot, parcel, or tract of land or parts thereof into four (4) lots or less, parcels or tracts, plus the residual parcel, which includes no extension of public sewer and water lines, streets, or other public improvements. The application may be classified as a minor subdivision or minor land development, provided that all of the following criteria are met:

A.	The proposal does not involve the extension of any public facilities including:

- New streets, access easements or any rights-of-way, or extensions thereof;

- Paving or other public improvements;

- New or improved water lines, or revised sewer lines or storm drainage facilities;

- New or improved or additional public facilities or services, or;

B.	The proposal does not conflict with the Township comprehensive plan.

C.	If a subdivision contains not more than four (4) lots, sites or other divisions of land, plus a residual parcel, and such subdivision or land development meets criteria as stated above, then it will be a minor subdivision. The applicants will indicate if this is a minor or major subdivision on their application.

106.2	Major Subdivision: Any subdivision that does not qualify as a minor subdivision.

106.3	Mobile Home Park: Shall be considered a parcel (or contiguous parcels which have been consolidated) of land which has been so designated and improved that it can accommodate two (2) or more mobile home lots for the placement thereon of mobile homes.

106.4	Land Developments: Certain land developments as described by and in this Ordinance and the MPC are land developments and are regulated by Article VIII of this Ordinance.

Section 107 Legal Standing

A.	If any section, clause, paragraph, regulation or provision of this Ordinance is found invalid by a court of law, such judgment shall not affect, impair, invalidate, or nullify the remaining sections, clauses, paragraphs, regulations, or provisions.

B.	All ordinances or parts of ordinances or regulations in conflict with this Ordinance or inconsistent with its provisions are hereby repealed to the extent necessary to give this Ordinance full force and effect. However, where another ordinance, law or regulation imposes a higher standard in a particular regulation, that standard shall supersede this Ordinance in the particular instance.

C.	Approval of any subdivision plan or land development is only approval of the specifications and regulations governed by this Ordinance.

Section 108 Unlawful Recording or Sale of Lots

A.	No plan of a subdivision or land development proposed within Hanover Township shall be recorded in any public office unless or until that plan has been approved or reviewed by the Board of Supervisors and shall bear the proper certification of such action.

B.	It shall be unlawful for any person to sell, trade or otherwise convey or offer to sell, including an agreement of sale, trade, or otherwise convey* any lot, parcel, or tract of land as part of, or in conformity with, any plan, plat, or lot line revision of any subdivision or land development unless and until said plan, plat, lot line revision, or land development shall have been first recorded in the office of the Beaver County Recorder of Deeds.

*This includes an agreement for sale.

Section 109 Effective Date and Repealer

This Ordinance shall become effective on April 13, 2010 and shall remain in effect until modified or rescinded by the Township. This Ordinance shall supersede and replace all other conflicting regulations issued by the Township previous to the approval date of this Ordinance, specifically Ordinance 29 of 1994.

Section 110 Subdivision Administrator

The Board of Supervisors shall appoint a Subdivision Administrator. All applications and correspondence shall be directed to the Subdivision Administrator, and the Administrator shall be responsible for all communications from the Township to the developer, including notices of approval, disapproval, and conditional approval.

Section 111 Recording

The Township shall record all subdivisions, site plans, or mobile home park plans, as required by this Ordinance.

Article II

Definitions

Section 201 General Interpretations

Unless otherwise expressly stated, the following terms shall, for the purpose of this Ordinance, have the meaning indicated: words in the singular include the plural, and the words in the plural include the singular. The word “person” includes a corporation, unincorporated association and a partnership as well as an individual or any other legal entity. The words “shall” and “will” are mandatory; the word “may” is permissive. An “agency” shall be construed to include its successors or assigns. Some words in this Article are defined by the Pennsylvania Municipalities Planning Code (PaMPC). It is the intent of this Ordinance to follow the PaMPC definitions; such words are noted with (PC).

Section 202 Meaning of Words

Alley: A minor right-of-way, publicly or privately owned, primarily for vehicular service access to the back and sides of properties. Alleys are not intended for through vehicular traffic.

Applicant: A landowner or developer, as hereinafter defined, who has filed an application for development including his heirs, successors and assigns. (PC)

Application for Development: Every application, whether preliminary, tentative or final, required to be filed and approved prior to the start of construction or development including, but not limited to, an application for a building permit, for the approval of a subdivision plat or plan, a mobile home park, or for the approval of a land development plan. (PC)

Approving Authority: The Hanover Township Board of Supervisors (unless otherwise specified).

Average Daily Trips (ADT): The average number of vehicular trips generated by a land use over a twenty-four (24) hour period during the week. Also quoted as AADT (Annual Average Daily Trips).

Block: An area divided into lots and usually bounded by four (4) roads.

Board of Supervisors: The Board of Supervisors of Hanover Township, Beaver County, Pennsylvania.

Building: A roofed structure, whether or not enclosed by walls, to be used for the shelter, enclosure, or protection of persons, goods, materials, or animals.

Cartway: The improved surface of a street or alley designed for vehicular traffic. Does not include shoulders or surface outside the gutter line.

Clear Sight Triangle: A triangular area of unobstructed vision at street intersections defined by lines of sight between points at a given distance from the intersection of street center lines.

Commission: The Planning Commission of the Township of Hanover.

Common Open Space: A parcel or parcels of land or an area of water, or a combination of land and water within a development site and designed and intended for the use or enjoyment of residents of a development, not including streets, off-street parking areas, and areas set aside for public facilities. (PC)

Condominium: A building or group of buildings, in which dwelling units, offices, or floor area are owned individually, and the structure, common areas, and facilities are owned by all the owners on a proportional, undivided basis.

Corner Lot: A lot, located at the intersection of two (2) or more existing or proposed street rights-of-way.

County: The County of Beaver, Pennsylvania.

Cul-de-Sac: A street intersecting another street at one end and terminating at the other in a vehicular turnaround.

Cut: An excavation. The difference between a point on the original ground and a designated point of lower elevation on the final grade. Also, the material removed in excavation.

Department of Environmental Protection (DEP): The Pennsylvania Department of Environmental Protection, its bureaus, divisions, departments and/or agencies, as may, from time to time, be established, or such Department or Departments as may, in the future, succeed it.

Detention Basin or Pond: An area in which surface water runoff is temporarily stored pending its release at a controlled rate.

Developer: Any landowner, agent of such landowner or tenant with the permission of such landowner, who makes or causes to be made a subdivision of land or a land development. (PC)

Development Plan: The provisions for development, including a planned residential development, a plat of subdivision, a land development, all covenants relating to use, location and bulk of buildings and other structures, intensity of use or density of development, streets, ways and parking facilities, common open space and public facilities. The phrase “provisions of the development plan” when used in this Ordinance shall mean the written and graphic materials referred to in this definition. (PC)

Double Frontage Lot: A lot having its front and rear lot lines abutting the right-of-way of a street, sometimes called a reverse frontage lot.

Drainage: The removal of surface water or groundwater from land by drains, grading or other means, and includes control of runoff to minimize erosion and sedimentation during and after construction or development.

Drainage Facility: Any ditch, gutter, culvert, storm sewer or other structure designed, intended or constructed for the purpose of carrying, diverting or controlling surface water or groundwater.

Drainage Easement: The lands required for the installation of stormwater sewers or drainage ditches, or required along a natural stream or watercourse for preserving the channel and providing for the flow of water therein to safeguard the public against flood damage.

Driveway: A private vehicular passageway providing access between a street and a private parking area or private garage.

Dwelling Unit: Any structure, or part thereof, designed to be occupied as living quarters as a single housekeeping unit.

Easement: A grant of one (1) or more property rights, usually in a defined area, by the property owner to and/or for use by the public, a corporation, or another person or entity.

Engineer: A professional engineer licensed as such in the Commonwealth of Pennsylvania.

Erosion: The removal of surface materials by the action of natural elements.

Erosion and Sediment Control Plan: A plan showing all present and proposed grades and facilities for stormwater, drainage, erosion and sediment controls, and which is in accordance with this Ordinance and applicable County, State, and Federal laws and regulations (contact the Beaver County Conservation District).

Excavation: Any act by which earth, sand, gravel, rock or any other similar material is dug into, cut, quarried, uncovered, removed, displaced, relocated or bulldozed and shall include the conditions resulting therefrom.

Fill: Any act by which earth, sand, gravel, rock or any other material is placed, pushed, dumped, pulled, transported or moved to a new location above the natural surface of the ground or on top of the stripped surface and shall include the conditions resulting therefrom. The difference in elevation between a point on the original ground and a designated point of higher elevation on the final grade. The material used to make a fill.

Grading and Drainage Plan: A plan showing all existing ground features and proposed grading, including existing and proposed surface and subsurface drainage facilities, described by grades, contours, and topography.

Impervious Surface: A surface that has been compacted or covered with a layer of material so that it is highly resistant to infiltration by water.

Land Development: Any of the following activities: (PC)

A.	The improvements of one (1) lot or two (2) or more contiguous lots, tracts or parcels of land for any purpose involving:

- A group of two (2) or more residential or non-residential buildings, whether proposed initially or cumulatively, or a single nonresidential building on a lot or lots regardless of the number of occupants or tenure; or

- The division or allocation of land or space, whether initially or cumulatively, between or among two (2) or more existing or prospective occupants by means of, or for the purpose of streets, common areas, leaseholds, condominiums, building groups, or other features.

- See also Article I and Article V of the Pennsylvania Municipalities Planning Code.

B.	A subdivision of land.

C.	“Land development” does not include development which involves:

- The conversion of an existing single-family, detached dwelling or single-family, semi-detached dwelling into not more than three (3) residential units, unless such units are intended to be a condominium;

- The addition of an accessory building, including farm buildings, on a lot or lots subordinate to an existing principal building; or

- The addition or conversion of buildings or rides within the confines of an enterprise which would be considered an amusement park. For the purposes of this subsection, an amusement park is defined as a tract or area used principally as a location for permanent amusement structures or rides. This exclusion shall not apply to newly acquired acreage by an amusement park until initial plans for the expanded area have been approved by the proper authorities.

Landowner (or Owner): The legal or beneficial owner or owners of land including the holder of an option or contract to purchase (whether or not such option or contract is subject to any condition), a lessee, if he is authorized under the lease to exercise the rights of the landowner, or other person having a proprietary interest in land. (PC)

Lot: A designated parcel, tract or area of land established by a plat or otherwise as permitted by law and to be used, developed or built upon as a unit. (PC)

Maintenance Guarantee: Any financial security, acceptable under Article V of the Planning Code, which may be accepted by the Township of Hanover for the maintenance of any improvements required by this Ordinance.

Marginal Access Street: A service street that runs parallel to a higher-order street, which, for purposes of safety, provides access to abutting properties and separation from through traffic. May be designed as a local street or collector as anticipated daily traffic dictates.

Major Subdivision: Any subdivision not classified as a minor subdivision.

Marker: A metal stake placed to designate the boundary and corners of lots in the subdivision of land for the purpose of reference in land and property survey and to facilitate the sale of lots (see Section 603).

Minor Subdivision: If a subdivision contains not more than four (4) lots, sites or other divisions of land, plus a residual parcel, and such subdivision or land development meets criteria as stated in Section 106.1 of this Ordinance, then it will be a minor subdivision.

Mobile Home: A transportable, single-family dwelling intended for permanent occupancy, contained in one (1) unit, or in two (2) or more units designed to be joined into one (1) integral unit capable of again being separated for repeated towing, which arrives at a site complete and ready for occupancy except for minor and incidental unpacking and assembly operations, and constructed so that it may be used without permanent foundation. (PC)

Mobile Home Lot: A parcel of land in a mobile home park, improved with the necessary utility connections and other appurtenances necessary for the erection thereon of a single mobile home. (PC)

Mobile Home Park: A parcel or contiguous parcels of land which has been so designated and improved that it contains two (2) or more mobile home lots for the placement thereon of mobile homes. (PC)

Modification: When a subdivider can show that a provision of this Ordinance would cause unnecessary hardship if strictly adhered to, and where because of topographic or other conditions peculiar to the site, in the opinion of the Township a departure may be made without destroying the intent of such provisions, the Planning Commission may recommend and the Township Supervisors may authorize a modification.

Monument: A concrete, stone, or other permanent object placed to designate boundary lines, corners of property, and rights-of-way of streets and utilities, for the purpose of reference in land and property survey (see Section 603).

Multi-Family Dwelling: A building containing three (3) or more independent dwelling units.

Performance Guarantee: Any security, consistent with the criteria of Article V of the Pennsylvania Municipalities Planning Code that may be accepted as a financial guarantee that required improvements are satisfactorily completed.

Person: An individual, partnership, corporation, or other legally recognized entity.

Plan, Final: A complete and exact subdivision plan, mobile home park, land development site plan, or other plan prepared for official recording as required by statute and this Ordinance.

Plan, Preliminary: The preliminary drawing indicating the proposed layout of the subdivision, mobile home park or site plan to be submitted for consideration, as required by this Ordinance (see Article III).

Plan, Sketch: An informal plan indicating salient existing features of a tract and its surroundings and general layout of the proposed subdivision.

Planning Code or Pennsylvania Planning Code: The Pennsylvania Municipalities Planning Code, Act 247 of 1968, as amended by Act 170 of 1988 and such other amendments to same as may be adopted from time to time.

Planning Commission: The Planning Commission of the Township of Hanover, Beaver County, Pennsylvania.

Plat: The map or plan of a subdivision or land development, whether preliminary or final. (PC)

Public Grounds: Parks, playgrounds and other public areas, and sites for schools, sewage treatment, refuse disposal, and other publicly owned or operated facilities. (PC)

Public Hearing: A formal meeting held pursuant to public notice by the Township of Hanover.

Public Meeting: A forum held pursuant to notice under the Act of July 3, 1986 (P.L. 388, No. 84), known as the “Sunshine Act.” (PC)

Public Notice: Notice as required under the provisions of the Pennsylvania Municipalities Planning Code.

Reserve Strip: A narrow parcel of ground having inadequate area for building purposes separating a street or a proposed street from other adjacent properties.

Right-of-Way: Land dedicated for use as a public street, alley or crosswalk, which may also be used by sewer, water, storm sewer, electric, gas, telephone and cable system(s).

Runoff: The surface water discharge or rate of discharge of a given watershed after a fall of rain or snow that does not enter the soil but runs off the surface of the land.

Sewage Disposal System, Community: A system of piping, tanks or other facilities serving two (2) or more lots and collecting, treating and disposing of domestic sewage into a subsurface soil absorption area or retaining tank located on one or more of the lots or at another site.

Sewage Disposal System, On-Lot: A system of piping, tanks, or other facilities serving a single lot and collecting, treating and disposing of domestic sewage into a subsurface absorption area or a retaining tank located on that lot.

Sewage Enforcement Officer (SEO): For the purpose of this Ordinance, the term Sewage Enforcement Officer, or SEO, shall mean the agency/individual appointed by Hanover Township, Beaver County, Pennsylvania. (See also Township Ordinance #52.)

Sight Distance: The extent of unobstructed vision, in a horizontal or vertical plane, along a street, as defined in Section 502 of this Ordinance.

Site Plan: An accurately scaled land development plan that illustrates the existing conditions on a land parcel as well as depicting details of a proposed land development.

Sketch Plan: A preliminary plan and attendant documentation of a proposed subdivision plan or land development of sufficient accuracy to be used for the purpose of discussion and classification.

Slope: The face of an embankment or cut section; any ground whose surface makes an angle with the plane of the horizon.

Street: Includes street, avenue, boulevard, road, highway, freeway, parkway, lane, alley, viaduct, and any other ways or strips of land used or intended to be used by vehicular traffic or pedestrians whether public or private, and including the entire right-of-way.

Street Center Line: An imaginary line which passes through the middle of the right-of-way and the cartway simultaneously, or which is in the center of the right-of-way in cases where the cartway is not centered in the right-of-way.

Structure: Any man-made object having an ascertainable stationary location on or in land or water, whether or not affixed to the land. (PC)

Subdivision: The division or re-division of a lot, tract or parcel of land by any means into two (2) or more lots, tracts, parcels or other divisions of land including changes in existing lot lines for the purpose, whether immediate or future, of lease, partition by the court for distribution to heirs or devisees, transfer of ownership or building or lot development: Provided, however, that the subdivision by lease of land for agricultural purposes into parcels of more than ten (10) acres, not involving any new street or easement of access or any residential dwelling, shall be exempted. (PC)

Subdivision Administrator: The person appointed by the Hanover Township Board of Supervisors to administer this Ordinance.

Subdivision – Major: Any subdivision not classified as a minor subdivision.

Subdivision – Minor: Any subdivision abutting or accessible to, by a minimum fifty (50) foot right-of-way, an existing public street or road involving not more than four (4) lots plus residual land area which may also be a conforming lot for area and dimensions, parcels of land, or other division of which does not require a new street, the installation of sanitary sewers, stormwater sewers, water mains or pipes, or other public improvements.

Subdivision – Lot Line Revision: The change of a lot line between two (2) abutting existing parcels which does not create a new parcel and where such lot line change is in full compliance with this Ordinance, the Township of Hanover Zoning Ordinance and related ordinances, rules and regulations of Township.

Substantially Completed: Where, in the judgment of the Township Engineer, at least ninety percent (90%) (based on the cost of the required improvements for which financial security was posted) of those improvements required as a condition for final approval have been completed in accordance with the approved plan, so that the project will be able to be used, occupied or operated for its intended use. (PC)

Surveyor: A professional land surveyor, licensed as such in the Commonwealth of Pennsylvania.

Swale: A low-lying stretch of land characterized as a depression used to carry surface water runoff.

Temporary Turnaround: A temporary circular turnaround at the end of a road which terminates at or near the subdivision boundary bordering undeveloped land.

Township: The Township of Hanover, Beaver County, Pennsylvania.

Township Engineer: A professional engineer licensed as such in Pennsylvania, duly appointed as the Engineer of the Township of Hanover or his/her representative.

Traffic Impact Analysis: An analysis prepared by a professional engineer of traffic generated by a new or expanded development plan on roads that provide access to the development.

Trip: A single or one-way vehicle movement to or from a property or study area. “Trips” can be added together to calculate the total number of vehicles expected to enter and leave a specific land use or site over a designated period of time.

Undeveloped Land: Any lot, tract, or parcel of land which has not been graded or in any other manner prepared for the construction of a building or other improvement.

Utility Plan: A plan to show all existing and proposed fire hydrants, water and sewer lines, storm sewer lines, gas and electric lines, cable television facilities, and street lighting.

Watercourse: A permanent stream, intermittent stream, river, brook, creek, or a channel, drain, or ditch for water, whether natural or man-made.

Article III

Procedures – Major Subdivisions, Minor Subdivisions,

Mobile Home Parks, and Land Developments

Section 301 Introduction

The purpose of this Section is to set forth the procedures for the submission, processing, and approval of, major subdivisions, minor subdivisions, mobile home parks, land developments, and other developments covered by this Ordinance. Generally, the processing will follow similar steps, although the details on the specific information, drawing scale, and other item may vary. For general information, the following is provided:

Minor Subdivisions and Lot Line Revisions: This Ordinance allows a streamlined processing for uncomplicated subdivisions. Generally, these involve small subdivisions along existing roads, and changes of lot lines between adjoining properties. No new utilities or roads are involved. A one-step process may be permitted starting with the final plan. Minor subdivisions and lot line revisions are defined in Article II.

Major Subdivisions, Mobile Home Parks and Land Developments: This is a two-stage process, using a preliminary and final plan. The purpose of the preliminary plan is to set forth the proposed development in detail. This allows for a comprehensive review of the proposed development to acquaint the developer with any requirements that may have been missed.

The final plan, be it a subdivision, mobile home park, or land development, is the document to be officially recorded. If all deficiencies have been corrected, the final plan can be approved.

Note: After approval, the completed subdivision plat will be recorded by the Township within ninety (90) days.

Section 302 Procedures for Major Subdivisions, Minor Subdivisions, Lot Line Revisions, Mobile Home Parks, and Land Developments

A.	Minor subdivisions and lot line revisions shall proceed directly to the final plan phase if they meet the standards as set forth by this Ordinance.

B.	Major subdivisions, mobile home parks, land developments, and other developments shall all use the two-stage process, that is a detailed preliminary plan followed by a final plan submission.

Section 303 Determination of Minor Subdivisions and Lot Line Revisions

A.	A subdivision may be classified as minor if it meets the requirements of the definition of same as contained in this Ordinance, does not violate the Township zoning ordinance or any other ordinance of this municipality. This designation may be denied if the parcel presents unique developmental issues as determined by the Subdivision Administrator. Such issues, however, must be clearly spelled out, in writing, and that determination mailed to the applicant.

B.	A lot line revision must meet the requirements as set forth by the definition of same contained in this Ordinance.

Section 304 Approving Body

For the purpose of this Ordinance, the Board of Township Supervisors is the approving body. However, all plans, be they preliminary or final, must be referred to the Hanover Township Planning Commission and the Beaver County Planning Commission.

By law, the County has up to thirty (30) days to complete its review and submit comments prior to action by the Board of Supervisors. [See 502(b) of the Planning Code.]

Section 305 Fees

Fees for the processing of subdivisions in the Township of Hanover are set by resolution of the Township Supervisors. Any fee for the County review is set by that agency. Such fees are the responsibility of the developer.

Section 306 Sketch Plan/Pre-Submission Conference

A sketch plan/pre-submission conference is not required. However, for a major development, it is highly recommended. The purpose is to acquaint the developer with the requirements of this Ordinance and to avoid unneeded processing or incorrectly prepared plats. This step may also be helpful for minor subdivisions as the developer or the developer’s surveyor may not understand the requirements of this Ordinance.

Section 307 Submission of Plans

All plans, preliminary or final, including those for mobile home parks or land developments, shall follow the following steps unless specifically exempted by this Ordinance:

307.1	Time of Submission: All plans must be submitted at least two (2) weeks prior to the meeting of the Hanover Township Planning Commission.

307.2	Number of Copies: At least nine (9) copies of the plan and four (4) copies of all required exhibits and one (1) application must be submitted. The size, scale, and type of submission are detailed by Article IV.

307.3	Subdivision Administrator: All plans, exhibits, applications and correspondence shall be directed to the Subdivision Administrator. The Subdivision Administrator is also responsible for all communications from the Township, including notices of approval, disapproval and conditional approval.

307.4	Receipt: The Subdivision Administrator shall review submissions to determine if all required components, including fees, are included. If they are not, the incomplete submission will be returned, and it will not be considered as a formal submission. If all required components are included, a receipt will be issued. The Subdivision Administrator has five (5) business days to complete this review. Any missing requirements, including required fees, will be listed in any letter of rejection. Note: The receipt acknowledges only that the submission is complete and does not determine its compliance with the standards set forth in this Ordinance or other applicable regulations.

307.5	Time: The Board of Supervisors shall take final action on the plan no later than ninety (90) days following the date of the next regular meeting of the Township Planning Commission following the date that a complete application is filed with the Township, provided, however, that should the next regular meeting occur more than thirty (30) days following the filing of the application, the ninety- (90) day period shall then be measured from the thirtieth (30th) day following the day the application was filed.

307.6	Processing: All plans, whether preliminary or final, shall be processed as follows:

A.	One (1) copy shall be sent to the Township of Hanover Planning Commission. The Commission shall review same for compliance with this Ordinance, any other pertinent regulations, and forward its recommendations to the Board of Township Supervisors.

B.	Two (2) copies shall be forwarded to the Beaver County Planning Commission for their review and comment. The plan shall not be approved until comments are received from that agency or the expiration of thirty (30) days from the date the application was forwarded. If the County imposes a fee for its review and report, that fee shall be paid by the applicant.

C.	Two (2) copies shall be sent to the Township Engineer for review and comment.

D.	Two (2) copies shall be retained to record approval, disapproval or conditional approval upon.

E.	The remaining copies shall be distributed as needed.

F.	After the developer has received official notification that a preliminary plan has been approved or conditionally approved and what changes, if any, must be made if the plan is to proceed to consideration as a final plan and has accepted these conditions, the developer has five (5) years in which to submit a final plan. If the developer does not do so within the five- (5) year period, the approval of the preliminary plan shall become null and void unless an extension of time is requested by the developer, in writing, and is granted, in writing, by the Township before the expiration date. [See also Section 508(4)(v) of the Planning Code.]

G.	Phasing: It is not necessary for the whole plan that received preliminary approval to be submitted as a final plan. The final plan may be submitted in sections, each covering a portion of the entire proposed subdivision shown on the preliminary plan. In the case where development is projected over a period of years, the Township may authorize submission of final plats by sections or stages of development subject to such requirements or guarantees as to improvements in future sections or stages of development as it finds essential for the protection of any finally approved section of the development. [See also Sections 508(4)(v) and 508(4)(vi) of the Planning Code.]

307.7	Time Extensions: If the applicant desires a time extension for preliminary or final plan approval, a written request shall be made to the Township. The request shall specify the reasons for the extension. The Township may grant time extensions and they shall be for a period of sixty (60) days. Additional requests for extensions may be made.

307.8	Approval, Disapproval or Conditional Approval: All actions shall take place at a public meeting. The Board of Supervisors of Hanover Township is vested with the power to:

A.	Approve the plan as submitted.

B.	Disapprove the plan as submitted. If the application is disapproved, the Board of Supervisors shall cite the deficiencies of the application and identify appropriate sections of this Ordinance which the application did not comply with.

C.	Conditional Approval: The Board of Supervisors of Hanover Township may grant the application a conditional approval. If so, it shall specify the defects found in the application and those sections of this Ordinance or law involved, as appropriate, and what other conditions must be met for approval. These conditions shall be forwarded to the applicant and must be accepted by the applicant, in writing, within twenty (20) days of notice thereof. If not accepted in writing, or if rejected, the conditional approval shall be rescinded and considered disapproved.

307.9	Prior to the approval of the final plan, a fully approved planning module for land development or non-building waiver(s) by the Pennsylvania Department of Environmental must be presented.

307.10	Notice of Action: The Subdivision Administrator shall notify the applicant, in writing, by first class mail, of the decision of the Board of Supervisors of Hanover Township within fifteen (15) days of the decision.

Section 308 Recording of Plan

A.	After completion of all procedures and upon approval of the final plan, the plan shall then be recorded with the County Record of Deeds. In no case shall the final plan be recorded after ninety (90) days from the date of the final plan approval. The Township shall record the plan and the developer/applicant shall be responsible for any fees or costs incidental thereto.

B.	The final plan shall be recorded with the County Recorder of Deeds before proceeding with the sale of lots, the issuance of building permits by the Township of Hanover or the construction of buildings. Proof of such recordation shall be required by the Code Officer.

C.	Recording the final plan after approval shall have the effect of an irrevocable offer to dedicate all public streets and other public ways to public use, and to dedicate or reserve all park reservations, and school sites and other public service areas as provided. Approval shall not impose any duty upon the Township of Hanover concerning maintenance acceptance or improvement of any such dedicated streets, parks, areas of portions of same until the proper authorities of the Township shall have made actual acceptance of the same by ordinance.

Article IV

Plan Requirements

The purpose of this Article is to set forth the information to be submitted in a sketch, preliminary, or final plan.

Section 401 Sketch Plan

The submission of a sketch plan is voluntary and is meant as an informational matter, not as a formal submission of a preliminary or final plan.

401.1	A subdivision sketch plan may be submitted by the developer or property owner as a basis for informal discussion with the Planning Commission, Subdivision Administrator, and Board of Supervisors.

401.2	Though the sketch plan need not be to scale and precise dimensions are not required, it should be accurate enough for a reasonable review. It is suggested that the following items be included in the sketch plan presentation:

-	Subdivision boundary

-	North arrow

-	Streets on and adjacent to the tract

-	General topographical and physical features (as required) – USGS maps are sufficient

-	Proposed general street layout

-	Proposed general lot layout

-	Proposed easements

-	Surrounding property and the names of owners

-	Name, address and telephone number of the surveyor, and, if needed, engineer

-	Existing zoning district, zoning district boundary lines or nearby zoning district boundary lines in the subdivision

-	Information relative to sanitary sewage, potable water, and storm drainage

The above sketch plan is for the purpose of a subdivision and mobile home park. Sketch plans for land development should include pertinent data per Article VIII.

Section 402 Preliminary Plan

402.1	A preliminary plan is required for major subdivisions (see Section 306).

402.2	The preliminary plan shall be drawn at a scale of one inch equals one hundred feet (1" = 100'). If the preliminary plan is drawn in two (2) or more sections, it shall be accompanied by a key map showing the location of the various sections. The size of the preliminary plans shall be twenty-four by thirty-six inches (24" x 36") in size for all subdivisions.

402.3	See Table 402.A./403.A

402.4	The following certificates, where applicable, shall appear on the preliminary plan. Suggested formats are in the Appendix.

A.	Certificate for the approval of the Board of Supervisors.

B.	Certificate for review of the Hanover Township Planning Commission.

C.	Certificate for review of the Beaver County Planning Commission, in such form as they may require.

D.	When the proposed development extends into another municipality, county, or state, any needed additional certification(s) shall be included.

E.	Certificate of the surveyor as to the accuracy of the survey and the engineer (if required) as to the accuracy of the design.

F.	Proof of ownership certification.

402.5	Phased Development: Developments may be submitted in phases. If the developer decides to submit in phases, then, with the initial submission, an overall sketch or preliminary plan is required showing the overall development plan, the location of street, water, sanitary sewer, storm drains, and other improvements. The submission shall delineate the number of phases and their estimated submission date.

Phased submissions shall comply with Section 503(4)(vi) of the Pennsylvania Municipalities Planning Code.

| Table 402A/403A Preliminary/Final Plan Checklist |
| --- |
|  |  | Preliminary | Final | Minor |
| 1 | Plan Name (Preliminary or Final) |  |  |  |
| 2 | Name, Address, and Phone Number of Owner |  |  |  |
| 3 | Agent (if any) |  |  |  |
| 4 | Proof of Ownership (current deed) |  |  |  |
| 5 | Date, North Arrow, Graphic Scale |  |  |  |
| 6 | Development Size, Lot, Lot Size, Size of Residual Lot |  |  |  |
| 7 | Track Boundaries, Distance, and Bearings |  |  |  |
| 8 | Zoning Designation |  |  |  |
| 9 | Floodplain Delineation |  |  |  |
| 10 | Location Map Inset (6" x 6") |  |  |  |
| 11 | Existing Building(s) to Scale |  |  |  |
| 12 | Names of Adjacent Owners and Adjacent Subdivisions, with Tax Parcel Numbers |  |  |  |
| 13 | Location and Dimensions of Features |  |  |  |
| 14 | Full Development Plan |  |  |  |
| 15 | Planning Module Component (On-Lot Sewage) |  |  |  |
| 16 | Public Water System Information |  |  |  |
| 17 | Community Sewer System Information |  |  |  |
| 18 | Design, Location of Other Utilities (separate sheets allowed) |  |  |  |
| 19 | Cross Section/Centerline Profiles of any Proposed Roads |  |  |  |
| 20 | Curbs/Sidewalks |  |  |  |
| 21 | Drainage Plan – Culverts and Swales |  |  |  |
| 22 | Design of Bridge Culverts |  |  |  |
| 23 | E & S Plan |  |  |  |
| 24 | Certificate (Surveyor/Engineer) |  |  |  |
| 25 | Lot Number(s) |  |  |  |
| 26 | Closure 1:10,000 Feet or Better, Closure Calculations |  |  |  |
| 27 | Complete Curve Data |  |  |  |
| 28 | Markers and Monuments (location and type) |  |  |  |
| 29 | Easements (20' required) |  |  |  |
| 30 | Accurate Description of Any Public Land |  |  |  |
| 31 | Street Names (Postmaster/Fire Marshal) |  |  |  |
| 32 | Source of Title, Deed Book and Page |  |  |  |
| 33 | State Plan, Coordinate System Reference |  |  |  |
| 34 | Stormwater Plan Endorsement |  |  |  |

Note:  indicates required element

Explanatory Material (as needed)

5.	Please note the graphic scale shall be one inch equals one hundred feet (1"= 100').

6.	The size of the development, the lots, and the residual lot shall be given in acres to the hundredths (example – 4.12 acres) or in square feet to the hundredth of a square foot (example – 22,507.52 square feet).

7.	Tract boundaries shall be set forth in feet to hundredths, and bearings to the second.

9.	Floodplain delineation shall be from the most recent FEMA maps available.

13.	Features – The locations and dimensions of all existing streets, easements, roads, railroads, public sewers, aqueducts, water mains, and feeder lines, fire hydrants, gas, electric, communication and oil transmission lines, streams, intermittent drainage ways, swales, and other significant natural features within the property proposed to be subdivided, and, where available, in the public domain within two hundred (200) feet of said property.

14.	Full Development Plan – A full plan of the development, showing the location of all proposed streets, roads, utility easements, parks, playgrounds, pedestrian ways, and other public areas, sewer and water facilities; proposed lot lines and dimensions of lots, including lot area; lot numbers and all streets and other areas designed for ancillary facilities, public use, or future public use, together with the conditions of such dedications or reservations.

15.	Planning Module Components for the Pennsylvania Sewer Facilities Act 537 on-lot sewage disposal system, if applicable, and the current status of the processing of same. The location of test pits. Status of any required DEP sewer system permits (as applicable), including permits or approvals for sanitary sewage system line extension, as well as any needed approval of the appropriate agency engineer.

16.	In addition to compliance with any authority, agency, or Township standards (as appropriate), any water system shall show compliance with DEP standards. A letter from any water supplier stating there is an adequate water supply will be required.

17.	In addition to compliance with any authority, agency, or Township standards (as appropriate), any sanitary sewer system shall show compliance with DEP standards. Also, a letter stating the sewer system has adequate capacity for the proposed development will be required.

19.	Street design shall be on separate pages.

20.	Curbs and Sidewalks –Hanover is a rural community and most developments will have neither curbs nor sidewalks where curbs are installed that shall be wedge curbs. Maintenance of any sidewalks constructed shall not be the responsibility of the Township. All such improvements shall comply with the Township’s Public and Private Improvement Code.

21.	Drainage Plan-Culverts and Swales – See the Township Public and Private Improvement Code.

22.	Design of Bridge Culverts – See the Township Public and Private Improvement Code.

23.	E & S Plan – See the Beaver County Conservation District and plan endorsement, as needed.

29.	Easements – All utility easements shall be centered on the utility, stream, or drainage. Easements may need to be increased, depending on site conditions.

31.	Street Names – The developer shall consult with the postmaster and/or fire marshall to avoid confusion or duplication of street names and locations, in the interest of public safety.

Section 403 Final Plan

403.1	A final plan is required for all subdivisions. (See Section 307 for processing.)

403.2	The final plan original for all subdivisions shall be drawn on stable plastic film.

403.3	Sheet size for final plans shall be twenty-four by thirty-six inches (24" x 36") in size for all subdivisions.

403.4	If the final plan is drawn in two (2) or more sections, it shall be accompanied by a key map showing the location of the several sections.

403.5	The final plan shall be drawn at the scale of one inch equals one hundred feet (1" = 100').

403.6	See Table 402A/403A.

403.7	The following certificates, where applicable, shall be shown on the final plan:

A.	Certification, with seal, by a registered land surveyor and/or engineer, as appropriate, to the effect that the survey and engineering plans are correct.

B.	Certificate for approval by the Board of Supervisors of the Township of Hanover.

C.	Certificate of review of the Hanover Township Planning Commission.

D.	Certificate for review of the Beaver County Planning Commission, in such form as they may require.

E.	When the proposed development extends into another municipality, county, or state, any needed additional certification(s) shall be included.

F.	A statement, duly acknowledged before a notary public, with seal, and signed by the owner or owners of the property, to the effect that the subdivision or development shown on the final plan is the act and deed of the owner, that he/she is the owner of the property shown on the survey and plan, and that he/she desires the same to be subdivided or developed and recorded as shown. Said statement to include an offer of dedication of public roads, easements or other improvements as needed.

G.	A certificate to provide for the recording of the subdivision or other plan.

H.	A highway occupancy permit notice when so required. See also Section 508(6) of the Pennsylvania Municipalities Planning Code.

403.8	The following information, in addition to that shown on the final plan, shall be submitted to the Township for final plan review, when applicable. Four (4) copies shall be submitted unless noted otherwise.

A.	Application for approval.

B.	Approval of the Township Engineer for public water, streets and storm drain systems, or required assurances of completion (see Section 1002). [One (1) copy]

C.	Approval by appropriate agencies of sanitary sewer systems. [One (1) copy]

D.	Approval by appropriate agencies of public water systems. [One (1) copy]

E.	Draft of any proposed covenants, easements, and/or rights-of-way to run with land.

F.	Tentative timetable for the proposed sequence of development for the subdivision, if required.

G.	Certificate of dedication of streets and other public property. This is the offer of dedication.

H.	Final profiles, cross sections, and specifications for street improvements, and sanitary and storm sewerage, and water distribution systems shall be shown on one (1) or more separate sheets. (Number of copies the same as Section 403.1.) Street design cross sections shall be provided at intervals of not less than fifty (50) feet for most roads. If a road’s grade is in excess of six percent (6%), the Township may require cross sections at closer intervals. [Two (2) copies]

I.	Other requirements of this Ordinance, as applicable.

Section 404 Additional Requirements

“As built” drawings shall be submitted for any improvements to be accepted by the Township or any Township authority.

Note: All fees and costs shall be paid prior to final approval.

Article V

Design Standards

Section 501 General

The design standards set forth by these regulations are intended to insure proper development in the Township.

501.1	The following land subdivision principles, standards, and requirements shall be applied by the Township in evaluating the plans for proposed subdivisions and shall be considered minimum requirements.

501.2	In reviewing subdivision plans, the Township will consider the adequacy of existing or proposed community facilities to serve the proposed development.

501.3	The subdividing of land shall be done in a manner that will not have the effect of debarring adjacent property owners from access to the streets and ways of the allotment. The Township may require dedicated, improved, or undedicated parcels to be provided for future access to adjacent land.

501.4	Land which is unsuited for development due to hazards such as flooding or the presence of steep slopes shall not be developed, though such land can be included in a subdivision.

A.	Land subject to flooding or which, if developed, will aggravate flooding conditions upon other lands.

B.	Landslide Prone Areas: In areas where soils or underlying geology may be unstable, geo-technical investigation may be required. Said geo-technical reports must be completed and signed by a licenses professional engineer.

501.5	Proposed subdivisions and land developments shall be coordinated with existing nearby neighborhoods or developments so that the community, as a whole, may develop harmoniously.

501.6	Proposed land uses and lot sizes shall conform to the Township of Hanover Zoning Ordinance.

Section 502 Streets

502.1.A.	Minimum street right-of-way widths and cartway widths shall be as follows:

| Type of Street | Cartway3 With Curbs | Cartway2 No Curbs | Right-of-Way | Shoulders |
| --- | --- | --- | --- | --- |
| Cul-De-Sac1 | 24 Feet* | 20 Feet | 50 Feet | 4 Feet |
| Minor/Local | 24 Feet* | 20 Feet | 50 Feet | 4 Feet |
| Collector | 36 Feet | 22 Feet | 60 Feet | 8 Feet |
| Industrial/Commercial | 36 Feet | 28 Feet | 60 Feet | 8 Feet |
| Arterial | As prescribed by the Pennsylvania Department of Transportation Design Standards. |
| 1 Residential; other cul-de-sacs follow other commercial or industrial standards 2 Requires shoulders 3.“Wedge curbs” are required – shoulders not required * Two 12-foot traffic lanes |

To determine the classification of a residential street, the following two tables shall be used as a guide:

| Street Classification |
| --- |
|  | Projected Daily Volume Traffic Volume (ADT)* |
| Cul-De-Sac | 0-250 |
| Minor/Local | 0-1,000 |
| Collector | 1,000-3,000* |
| Source: Table 2-1, Residential Streets, 2nd edition, American Society of Civil Engineers, National Association of Home Builders, Urban Land Institute |

| Residential Trip Generation Rates Daily Vehicle Trips Per Dwelling Unit* |
| --- |
|  | Weekday | Peak Hour |
| Single-Family Detached | 10.0 | 1.0 |
| Apartments |  |  |
| All | 6.0 | 0.7 |
| Low Rise | 7.0 | 0.7 |
| High Rise | 4.0 | 0.4 |
| Townhouse and Single-Family Condominiums | 6.0 | 0.6 |
| Source: Table 2-2, Residential Streets, 2nd edition, American Society of Civil Engineers, National Association of Home Builders, Urban Land Institute (figures rounded) *The Township will accept updated traffic generation data from such sources as the Trip Generation Manual of the Institute of Transportation Engineers. |

Note: In the event the projected volume of a street exceeds three thousand (3,000) vehicles per day, then its design shall be based upon current PennDOT or other accepted engineering standards but in no event shall be less than the standards for a collector, as shown in 502.1.A.

502.2	In cases where a new subdivision is planned to join the street system on an existing subdivision, the above minimum requirements shall apply except where the existing streets and right-of-ways are larger than required. In this event, the Township may require that the new streets and right-of-ways be as large as those in the existing subdivision. Any street that is planned, though not already established shall be continued at not less than its width as planned.

502.3	Provisions for additional street width (right-of-way) may be required by the Township in specific cases for:

A.	Public safety and convenience.

B.	Parking in commercial and industrial areas and in areas of high-density residential development.

502.4	General design criteria for streets not otherwise covered in this Ordinance shall be in accordance with specifications as set forth by the Township and appropriate publications of the Pennsylvania Department of Transportation.

502.5	Cul-De-Sacs

A.	In no event shall a street be allowed to dead end without a permanent cul-de-sac.

B.	Residential dead-end streets (cul-de-sacs) may be permitted when it is clear that through traffic is not essential. A dead-end street must have adequate turning space for vehicles, which shall include a minimum right-of-way radius of fifty (50) feet, and a minimum road edge (excluding shoulders) or curb radius of forty (40) feet. The entire turnaround area is to be paved. Full pavement shall extend to the outer edge of the forty (40) foot radius. In no event shall the shoulder area be considered as part of the required minimum road width. Cul-de-sacs shall be signed with a “No Outlet” sign for ingress traffic and a “Stop” sign for egress traffic. In no event shall a cul-de-sac serve more than twenty-five (25) dwelling units, or exceed one thousand (1,000) feet in total length.

Cul-de-sacs for commercial or industrial developments shall be designed to allow for the turn of a full-sized tractor trailer combination as allowed by the Commonwealth of Pennsylvania.

502.6	Street intersections shall comply with the following requirements:

A.	All curbs or pavement outer edge at intersections shall be rounded by a minimum radius of:

| Collector, Commercial, and Arterial | 40 Feet |
| --- | --- |
| Minor, Local Streets | 25 Feet |
| Industrial Streets | 50 Feet |

Thirty- (30) foot radii shall be used where minor streets intersect collector and/or arterial streets.

B.	When visual obstructions on any lot corner within the development would create a traffic hazard by limiting clear vision across a corner lot from a height of three (3) feet above the finished paved area, at the center line of the right-of-way, such structure and/or vegetation shall be removed in conjunction with grading the right-of-way to provide a minimum sight line in a clear sight triangle:

1.	Seventy-five (75) feet from the point of intersection of the center lines of two (2) streets where both are minor streets.

- One hundred (100) feet from the point of intersection of the center lines of two (2) streets where one is a collector street.

- One hundred fifty (150) feet from the point of intersection of the center lines of two (2) streets where one is an arterial street.

When an arterial, commercial, industrial or collector and a minor street intersect, each shall retain its respective footage requirements along the center line to form the sight triangle. No building or structure shall be permitted in this sight triangle. Sight triangles shall be shown on the plan. (See also the Public and Private Improvement Code)

C.	Where the grade of any street at the approach to an intersection exceeds four percent (4%), a leveling area shall be provided, with a transitional grade not to exceed three percent (3%) for a minimum distance of fifty (50) feet from the nearest right-of-way line of the intersection.

D.	Intersections of more than two (2) streets shall not be allowed.

E.	Minimum street intersection angles shall be seventy-five (75) degrees. Right angle intersections shall be used whenever possible.

F.	Intersecting streets shall be separated by two hundred (200) feet or more, measured between center lines along the center line of the intersected street.

502.7	Horizontal curves shall be laid on all deflecting angles along the center line of streets, and the degree of curvature shall be set to assure the proper sight distance, as required by Table A.

502.8	Vertical curves shall be used in changes of grade exceeding one percent (1%), and shall be designed for maximum visibility as set forth by Table A.

502.9	In general, minor and collector streets shall not join into the same side of arterial streets at intervals of less than eight hundred (800) feet.

502.10	Half streets shall be prohibited.

502.11	The provisions for the extension and continuation of major streets into and from adjoining areas are required. Where a subdivision abuts or contains an existing or proposed collector street, the Township may require reverse frontage lots or such treatments as will provide protection for abutting properties, reduction in the number of intersections with the major traffic streets, and separation of local and through traffic.

502.12	When the subdivision adjoins un-subdivided acreage, new streets or reserved right-of-ways may be provided through to the boundary lines of the development.

502.13 If the lots in a development are large enough for re-subdivision, or if a portion of the tract is not subdivided, suitable access and street openings for such re-subdivision shall be provided. Note: This will not apply if subject land is to be held as permanent dedicated open space. Such access or openings shall not be less than fifty (50) feet in width.

| Table A Design Criteria for Streets1 (Not to Include Intersections) |
| --- |
| Type of Street |
| Item | Comm./Ind. | Collector | Minor/Local | Cul-De-Sac4 |
| Maximum Grade2 | 6.0% | 6.0% | 12.0% | 10.0% |
| Minimum Grade | 1.0% | 1.0% | 1,0% | 1.0% |
| Minimum Centerline Radius | 500 Feet | 500 Feet | 250 Feet | 250 Feet |
| Minimum Sight Distance3 | 300 Feet | 300 Feet | 250 Feet | 250 Feet |
| Tangent Between Curves | 150 Feet | 150 Feet | 100 Feet | 100 Feet |
| 1 For Arterial Roads, PennDOT standards will apply. 2 Grades in excess of the allowable percentage may be approved by the Township where it is clear that it is necessary and that no traffic hazard is or will be created thereby. 3 Sight distance shall be measured along the center line of the street between points where a driver’s eyes at 3' 6" in height can see an object 6" high. Values shown are minimums. Greater values may be required depending on site specific criteria. 4 Please see cul-de-sac definition, a cul-de-sac is the entire street not merely the vehicular turnaround. |

  - All required traffic control devices, including required signs, shall comply with, and be installed in accordance with the current Commonwealth of Pennsylvania Department of Transportation, Title 67, Chapter 212 (or as it may be amended). Generally, it shall be the developer’s responsibility to perform all required Traffic and Engineering Studies in accordance with PennDOT standards.

  - Private streets may be authorized to permit limited subdivision of lots subject to the following requirements:

A.	A maximum of four (4) lots, plus a residual parcel containing one (1) existing residential structure, may be approved for access on a private street.

B.	The private street right-of-way shall be a minimum of fifty (50) feet, except as otherwise indicated.

C.	The street shall be installed to provide the required minimum width with a mud-free cartway in accordance with the design standards in item E below, which are adequate to enable all-weather passage of vehicles.

D.	Sales agreements for all lots abutting the private road shall include notification to purchasers of the non-liability of the Township for road maintenance, or related improvements. In addition, a certificate of the non-liability of the Township shall be inscribed on the plan when submitted for municipal approvals.

E.	The Township’s Public and Private Improvement Code shall detail the construction of these private roads. At a minimum, such roads shall:

- Have a minimum cartway width of twenty (20) feet.

- The road bed shall be composed of four inches (4") of rolled and compacted crushed aggregate.

- Have no grade in excess of twelve percent (12%).

- The required cul-de-sac road bed area shall be also composed of four inches (4") of rolled and compacted crushed aggregate.

- The right-of-way/cartway for private roads shall not be re-subdivided or diminished in any way.

F.	A temporary turnaround for maintenance and emergency vehicles shall be provided where future street or roadways extensions are designed to occur, said turnaround shall have a minimum sixty- (60) foot diameter curb to curb and be composed of four (4) inches of rolled and compacted crushed aggregate.

G.	A private maintenance agreement form provided by the Township shall be signed and recorded prior to the approval of the subdivision.

Section 503 Curbs and Sidewalks

503.1	Curbs: When curbs are installed, the following criteria are to be followed:

A.	Wedge curbs will be used.

B.	Where sidewalks are installed, curbs shall be depressed at intersections to sufficient width to accommodate wheelchairs. Depression shall be in line with sidewalks where provided. (Note: Appropriate Federal ADA standards will be followed.)

C.	All curbs and curb cuts shall be constructed in accordance with the Township’s Public and Private Improvement Code.

503.2	Sidewalks: Sidewalks may be provided for all major subdivisions where the average lot width is seventy-five (75) feet or less and for any minor subdivisions where sidewalks exist on abutting parcel(s). The width, depth, design and specifications for sidewalks shall comply with the current sidewalk standards of the Township. But, in no event shall sidewalks be less than five (5) feet wide.

Section 504 Blocks

504.1	Blocks shall be designed to insure proper fire safety.

504.2	In general, all blocks in a subdivision shall have a maximum length of one thousand six hundred (1,600) feet. Blocks subdivided into lots shall be approximately two (2) lot depths in width, except lots along a major thoroughfare which may front on an interior street. Block lengths shall not be less than six hundred (600) feet.

504.3	In commercial areas, the block layout shall conform with due consideration to site conditions, to the best possible layout to serve the public, to permit good traffic circulation and the parking of cars, to make delivery and pickup efficient, and to reinforce the best design of the units in the commercial areas.

504.4	The block layout in industrial areas shall be governed by the most efficient arrangement of space for present use and future expansion, with due regard for worker and customer access parking. Of special interest will be the accommodation of truck traffic.

Section 505 Lots and Building Lines

505.1	Double frontage and reverse frontage lots should be avoided except where essential to provide separation of residential development from traffic arterials or to overcome specific disadvantages of topography and orientation. A planting screen easement, across which there shall be no right of access, may be required by the Township along the line of lots abutting such a traffic artery or other disadvantageous use.

505.2	Side lines of lots, so far as practical, shall be at right angles or radial to street lines.

505.3	Lots abutting local streets shall front upon the streets which parallel the long dimension of the block, if possible.

505.4	All lots shall abut by their frontage on a publicly dedicated or approved private street (see also Township Zoning Ordinance).

Section 506 Lot Grading for Subdivisions and Land Developments

506.1	Blocks and lots shall be graded to provide proper drainage away from buildings and to prevent the collection of stormwater in pools.

506.2	Lot grading shall be of such design as to carry surface waters to the nearest practical street, storm drain, or natural water course. Where drainage swales are used to deliver surface waters away from buildings, their grade shall not be less than one percent (1%) nor more than four percent (4%). The swales shall be sodded, planted or lined as required. A grading and drainage plan shall be required for all subdivisions and land developments, except minor subdivisions.

506.3	No final grading, fill, or cut shall be permitted with a cut face steeper in slope than two (2) horizontal to one (1) vertical except under one or more of the following conditions:

A.	The material in which the excavation is made is sufficiently stable to sustain a slope of steeper than two (2) horizontal to one (1) vertical, and a written statement of a geo-technical engineer, who is qualified to prepare a geo-technical report, licensed by the Commonwealth of Pennsylvania and experienced in erosion control, to that effect is submitted to the Township Engineer and approved by same. The statement shall state that the site has been inspected and that the deviation from the slope specified hereinbefore will not result in injury to persons or damage to property.

B.	A retaining wall designed, certified, and sealed by a licensed professional engineer for which plans have been submitted and approved by the Township Engineer and written approval is provided.

506.4	The top or bottom edge of cut or fill slopes shall be a minimum of ten (10) feet from property or right-of-way lines of streets or alleys in order to permit the normal rounding of the edge without encroaching on the abutting property. All property lines, or right-of-way lines, where walls or slopes are steeper than one (1) horizontal to one (1) vertical and five (5) feet or more in height shall be protected by a protective fence no less than three (3) feet in height approved by the Township Engineer.

Section 507 Easements

507.1	Where a subdivision is traversed by a watercourse, drainage way, channel, or stream, a drainage easement may be required that conforms substantially with the water line of such watercourse, drainage way, channel, or stream and of such width as will be adequate to preserve the unimpeded flow of natural drainage, or for the purpose of widening, deepening, relocating, improving or protecting such drainage facilities.

507.2	Where desirable or necessary, adequate easements or dedications for public service utilities shall be provided for sewer, water, electric power, gas lines, storm drainage and similar services; and no structure or obstruction of any kind shall be placed or allowed to be placed where it will interfere in any way with such easements.

507.3	Utility and drainage easements, where required, shall have a minimum width of twenty (20) feet and be placed at the side or rear of lots whenever possible.

Section 508 Street Names

The developer shall work with the postmaster and/or fire marshall in assigning street names to avoid confusing or duplicated street names.

Section 509 Stormwater Drainage

All new roads shall provide storm drainage facilities in accordance with specifications as set forth by the Township Engineer, Hanover Township and/or applicable State or Federal law or regulation. All subdivisions shall provide a stormwater drainage plan.

Section 510 Utility Regulations for Subdivision and Land Development

Gas, electric, water, telephone, and cable utilities shall be located underground in major subdivisions in accordance with utility company standards and in accordance with all other requirements of the Township (see also Section 608).

Section 511 Floodplain Area Regulations

All developers are required to follow the Township’s or the State’s floodplain regulations. In addition, when any flood plains are located within a proposed development, they should be clearly identified on the preliminary and final plat. The developer will use the most recent floodplain information for the Township, as available from the Federal Emergency Management Agency.

Any public facilities or utilities which are constructed in a floodplain area shall be designed in accordance with approved regulations. These regulations are set forth in the Township’s floodplain regulations.

Section 512 Sanitary Sewer Systems

Sanitary sewer systems shall follow the design and construction criteria as set forth by the Pennsylvania Department of Environmental Protection and the Township, or appropriate Authority. All designs must demonstrate compliance with DEP permit requirements and secure DEP approval.

Section 513 Water Systems

Water systems shall follow the design and construction criteria as set forth by the Pennsylvania Department of Environmental Protection and the Township or appropriate Authority, and secure all needed approvals. All designs must demonstrate compliance with DEP and Agency requirements and/or permit standards.

Section 514 Landscaping and Street Trees (If required by the Board of Township Supervisors)

Any trees used as street trees shall be suited for the use intended and the Hanover Township area. The Township shall use standard references such as Street Trees: A Manual for Municipalities to review tree planting proposals. Street tree calipers shall be at least one-and-one-half inches (1½"). All landscaping shall be guaranteed for at least one (1) year, and any landscaping found dead or diseased in that one- (1) year period shall be replaced.

Article VI

Required Improvements

Section 601 General

  - The construction of subdivision and some land development improvements is the responsibility of the developer insomuch as it is his/her property which is being developed. Adequate streets, utilities, and other improvements are essential elements in the creation and preservation of stable residential, commercial, and industrial areas, and must be completed by the developer.

Construction specifications are set forth by the Public and Private Improvement Code that has been adopted by the Township.

Section 602 Improvements

602.1	Utility and street improvements shall be provided, where required, in each new subdivision as follows, except that improvements are not required in existing public streets which may be incorporated into, or be adjacent to, the subdivision.

A.	Survey monuments and markers

B.	Water supply

C.	Public or community sanitary sewage facilities

D.	Storm drainage facilities

E.	Streets, including required grading, subgrade preparation, sub-drainage, subbase,and pavement

F.	Curbing on streets (if required)

G.	Sidewalks (optional); if installed, seeding or sod between the sidewalk and curb.

H.	Required utilities, street lighting, street name signs and grading, as required

I.	Erosion and sedimentation control, as needed

J.	Site grading

Section 603 Monuments and Markers

603.1	Survey monuments and markers shall be placed at all points as determined by the following criteria. Monuments and pins will be regarded as part of the needed improvements for all subdivisions and must be installed prior to final plan approval.

A.	Monuments shall be in accordance with the Public and Private Improvement Code.

B.	Markers shall be ferrous metal rods, five-eights- (5/8) inch minimum diameter by thirty (30) inches minimum length or may be standard manufactured ferrous metal survey markers of a similar length.

C.	Monuments shall be placed by a registered surveyor so that the center point shall coincide exactly with the intersection of lines to be marked.

D.	Monuments shall be placed so that they are flush with the final grade, with the metal pin extending one-quarter (¼) inch.

E.	Markers shall be driven into the ground so as to be approximately flush with the final grade.

F.	Monuments shall be set at the intersection of all lines forming angles in the boundaries of major subdivisions. They shall also be set at the intersection of all street right-of-way lines.

G.	Markers shall be set at all lot angles and corners, and at the beginning and end of all curves in lot and street lines and at the angle points of all streets right-of-way(s).

H.	An escrow bond of one hundred fifty dollars ($150.00) per concrete monument must be delivered to the Township. When monuments are placed, approved by developer’s engineer and inspected by the Township Engineer, then the escrow bond will be released to the developer.

Section 604 Water Supply

If a development is within one thousand (1,000) feet of an existing water distribution system, the developer shall utilize that system for the development’s water supply. If the water supply system is unable to provide the needed service to the development, that fact must be clearly documented. Those developments beyond one thousand (1,000) feet distance will not be required to use same.

604.1	Prior to the approval of the preliminary plan, the developer shall provide documentation from the water agency that arrangements for the provision of the water system are proceeding satisfactorily.

604.2	Fire hydrants shall be provided concurrently with the construction of the water supply. The hydrants and location shall be approved by the local fire marshal.

604.3	All public water systems shall be laid wherever possible in the street right-of-way but outside the cartway and constructed in accordance with the standards of the water supplier and the Pennsylvania Department of Environmental Protection.

604.4	Upon completion of the water supply system, and before any person uses said water supply the subdivider shall submit two (2) copies of as-built plans to the water supplier. Said as-built plans shall show by stationing all valves, house taps, length and size of house connections and location of fire hydrants, position of mains in the right-of-way.

604.5	All inspection costs shall be borne and paid by the developer (see Sections 503 and 510 of the Planning Code).

Section 605 Sanitary Sewage Conveyance

If a development is within one thousand (1,000) feet of an existing public sewage collection system, the development shall utilize that system. If that system cannot accept the projected development flows, that fact must be fully documented. Developments using on-lot systems must comply with all appropriate local, State (and County) requirements.

605.1	The developer shall construct a sanitary sewer system and provide lateral connections for each lot in accordance with the specifications approved by the sanitary sewer agency. Construction shall also comply with the appropriate standards of the Pennsylvania Department of Environmental Protection. A sewer planning module shall be approved by the (sanitary sewer agency) and DEP prior to final plan approval.

605.2	The developer shall secure from the appropriate sanitary sewer agency engineer a letter indicating the general design, location and preliminary approval of the proposed sanitary sewer collection system. Prior to the acceptance of the facilities by the sanitary sewer agency, the developer shall supply documentation attesting to the proper installation of the sanitary sewer collection system.

605.3	In addition to the above-cited specifications, sanitary sewers shall:

A.	Be located in the right-of-way or an easement.

B.	Manholes: Manholes shall be set at all changes to line or grade and shall have a maximum spacing of four hundred (400) feet. (This may with slope vary with pipe diameter.)

C.	Storm sewers, where provided, shall not be connected with sanitary sewers.

D.	Footer drains, parking lot drains, or roof drains shall not be connected to the sanitary sewers.

605.4	All phases of construction, including excavation, trenching, installation of the appropriate size of pipe, grading, backfilling and installation of manholes shall be in accordance with construction drawings approved by the sanitary sewer agency, or the Public and Private Improvement Code, and the Department of Environmental Protection (if required) and shall be inspected by the sanitary sewer agency or Township Engineer, by his/her designation representative during the entire construction period. All inspection costs shall be borne by the developer in accordance with the provisions of Sections 503 and 510 of the Planning Code.

605.5	Upon completion of sanitary sewer installation, two (2) copies of each of the plans for such systems, as built, shall be filed with the sanitary sewer agency, said as-built plans shall show by stationing all manholes, laterals, length of laterals, top elevations and invert elevation and size and location of mains within the right-of-way.

Section 606 Storm Sewers: The design and construction of storm sewer systems are covered by the Hanover Township Public and Private Improvement Code and the Hanover Stormwater Management Ordinance.

Section 607 Streets, Cul-De-Sacs, Curbs, and Sidewalks

607.1	Streets, cul-de-sacs, curbs, and sidewalks shall be designed and constructed in accordance with the Township Public and Private Improvement Code.

607.2	The developer shall submit plans, profiles, cross-sections, and details for streets, cul-de-sacs, curbs, and sidewalks to the Township. The developer shall not initiate construction until such plans have been approved by the Township or the Township Engineer, including any revisions required by the Township and the Township Engineer. Construction of streets, cul-de-sacs, curbs, and sidewalks shall be in accordance with plans that have been approved by the Township.

607.3	All streets and cul-de-sacs shall have subdrainage systems consisting of subgrade (blind) drains and pavement base drains, designed and constructed in accordance with the Township Public and Private Improvement Code.

607.4	Specifications for industrial, commercial and other special use streets will be determined by the Township Engineer on a case-by-case basis, using current standards.

Section 608 Utilities

Gas, electric, telephone and cable utilities shall be located in subdivisions in accordance with utility company practice and in accordance with agreements with, or as approved by the Township. All buried utilities must be installed prior to the road subbase construction. All buried utilities located within the roadway must be backfilled with the same material and compaction requirements as specified for storm or sanitary sewer backfill within roadways.

Section 609 Erosion Control

It shall be a requirement of all major subdivisions and certain minor subdivisions (determined by the Beaver County Conservation District) that the developer shall have a Soil Erosion and Sedimentation Control Plan and/or permit, prepared in accordance with current state law (Erosion and Sedimentation Control, Chapter 102, Pennsylvania Rules and Regulations, as amended), which shall be reviewed and approved by the Beaver County Soil Conservation District or its successor organization. The Township may also require a like plan for any minor subdivision. The plan shall be fully implemented during the construction of the development. A copy of the approved Soil Erosion and Sedimentation Control Plan, along with the approval letter, shall be submitted with the subdivision plans.

Note: Township endorsement per E & S, stormwater, and wetlands is to appear on the plan.

Article VII

Mobile Home Park Regulations

Section 701 Applicability

No person, firm or corporation proposing to open, re-arrange or expand a mobile home park in the Township, shall proceed with any construction work on the proposed park until they have obtained from the Township written approval of the preliminary plan of the proposed development, according to procedures herein outlined.

Section 702 Plan Requirements

A.	Preliminary and final plans, as required, shall comply in form and content to Articles III and IV of these regulations in-so-far as applicable and shall be in accordance with the standards set forth herein.

B.	A stormwater management plan shall be submitted.

Section 703 Preliminary Plan

A.	Pre-Application Procedure: The mobile home park developer should meet with the Township, prior to formal application, to discuss his/her plans and should prepare a suitable sketch and plans sufficient to give a general understanding of his/her purposes. The Township shall inform the developer as to the general suitability of the plans and of any modifications required by these regulations, if deemed advisable.

B.	Application: The developer shall then prepare and submit a complete preliminary plan, together with improvement plans and other supplementary material, as required.

C.	Action: The Planning Commission and Board of Supervisors shall review the mobile home park plan as submitted and take actions as required in Article III.

Section 704 Final Plan Approval

A.	Upon completion of any modifications required by the Township and/or upon completion of required improvements or the alternate posting of acceptable surety, the developer may apply for approval of the final plan. Until the final plan for the mobile home park is approved and recorded and until all required improvements are completed for the mobile home park, the placement and habitation of individual mobile homes shall not be permitted [see Section 509(m) of the Planning Code].

B.	The Board of Supervisors shall review the final plan for conformance with the approved preliminary plans and all requirements of these rules and regulations. Where required, an appropriate bond must be posted or required improvements have been installed, according to specifications (see Articles IIII and X of this Ordinance).

C.	Filing: Following approval, the Township shall file one (1) copy of the approved plan with the Beaver County Recorder of Deeds within ninety (90) days. Any fees for recordation shall be borne by the applicant.

Section 705 Design Requirements

A.	Minimum Area of Tract or Park: The minimum area of the tract or park shall be ten (10) acres. The site shall be so located that soil conditions, groundwater level, drainage, and topography shall not create hazards to the property, health, or safety of the occupants or adjacent property owners. The overall density of the mobile home park shall not exceed two (2) units per acre of land.

B.	Individual Lots: The planning and location of individual lots shall be guided by the following requirements:

- Access: Each lot shall be directly accessible from an approved internal street or public road without the necessity of crossing any other space.

- Lot Suitability: No individual lot shall be developed for occupancy by a mobile home if the slope is eight percent (8%), or in excess of same.

- Size: This lot assumes a placement with the narrow side of the unit facing the street. Each mobile home lot shall have a minimum lot width of seventy (70) feet, depth of at least one hundred fifty (150) feet, and a minimum of twenty thousand (20,000) square feet in area. The developer can opt to place units with the “wide” side of the home facing the internal street.

- Yard Requirements:

a.	There shall be two (2) side yards; the minimum side yard shall be ten (10) feet and the second side yard fifteen (15) feet. Yards shall be oriented so the fifteen- (15) foot side yard shall be on the side of the dwelling unit where the patio or deck is located. This assumes the main entrance on a side yard. Where the “wide” side of the home faces the road, two (2), ten- (10) foot yards will be required:

(1)	The setback from the internal street cartway shall be at least thirty (30) feet. Parking for two (2) vehicles may be allowed in the front yard area; however, at least ten (10) feet shall be reserved for lawn or landscaping between the parking area and the dwelling unit.

(2)	The rear yard shall be at least thirty (30) feet in depth. Any utility or storage building is to be located in the rear yard at least ten (10) feet from any mobile home lot line and ten (10) feet from the dwelling unit. If the developer orients the units so the “wide” side faces the internal street, the required isolation distances must be observed.

b.	There shall be a minimum of twenty-five (25) feet between individual mobile homes, attached structures, and at least ten (10) feet to an accessory structure on the same lot, and at least twenty (20) feet to an accessory structure on another lot.

c.	The setback from the right-of-way of any public street or highway shall be consistent with the zoning ordinance district.

d.	There shall be at least forty (40) feet between any mobile home, appurtenance building, office or similar structure and any mobile home park boundary line.

5.	Skirting: The plans shall specify that skirting shall be provided on all mobile homes. Skirting shall be so designed as to allow for adequate ventilation under the mobile homes.

6.	Orientation: The developer is encouraged to enhance the design of the park and can vary unit orientation as long as lot size and setbacks as set forth in this Ordinance are followed. The Township may consider lot averaging when reviewing alternative designs.

- Landscaping: The park entrance shall be landscaped with a sign giving the name of the facility in a setting of shrubs and trees.

All internal streets shall be planted with street trees of at least one-and one-half (1½) inch caliper planted at fifty- (50) foot intervals. Street trees will be located on all sides of the street where mobile home units are located. The developer shall provide a planting schedule with the Township which must be approved by the Township Engineer.

A thirty- (30) foot wide landscape buffer shall be provided along the perimeter of the site. The landscape buffer shall consist of a mixture of both evergreen and deciduous trees and shrubs. The buffer shall provide a visual barrier and be composed of plants suitable to that purpose and of species suitable for this area. The buffer strip planting plan must be approved by the Township Engineer.

C.	Mobile Home Stands

- The location of each mobile home stand shall be at such elevation, distance and angle in relation to the access street so that the placement and removal of the mobile home is practical.

- The stand where the unit is placed shall be at least fourteen (14) feet by sixty-five (65) feet to accommodate modern units.

- A one percent (1%) to five percent (5%) gradient longitudinal crown or cross gradient for surface drainage shall be provided. Water shall be directed away from the mobile home stand. In no event shall the stand be designed to allow the pooling of water under mobile homes.

- All mobile homes shall be set on a foundation, as required by the Township’s building code, the Pennsylvania UCC.

- There shall be a concrete patio area provided for each stand, not less than ten (10) feet wide and twenty (20) feet long located convenient to the main entry door to the mobile home. The patio will be on the side of the lot with the fifteen- (15) foot side yard.

D.	Access and Internal Street System: The internal street system in privately owned mobile home parks shall be privately owned and maintained. It shall be constructed and maintained in accordance with the applicable sections set forth for public roads by the Public and Private Improvement Code. Mobile home parks shall provide at least one (1) access road to a public road for each twenty-five (25) mobile homes. These access roads shall be placed with the advice of local fire departments and emergency services to facilitate servicing all areas of the park. Internal streets shall have a paved cartway of at least twenty (20) feet in width.

E.	Street Widths at Access Points: At points where general traffic enters or leaves the park, streets shall be twenty-four (24) feet in width within twenty (20) feet of the existing public street to permit free movement from or to the stream of traffic on the public street, and no parking shall be permitted which in any way interferes with such free movement.

F.	Parking Spaces: Parking shall be provided in such amount as required by the Township’s zoning ordinance, but in no event shall there be less than two (2) parking places for each lot. These spaces may be located off interior streets and shall be paved or provided with a stone/gravel/ crushed limestone surface of at least six (6) inches in depth, compacted to provide a year-round mud-free parking area. There shall be a concrete or paved walkway from the parking area to the main entrance of the unit. In addition to the on-lot parking for every mobile home development with twenty-five (25) or more units, a visitors’ parking area shall be provided with one (1) space per each two (2) units. This parking lot shall be paved in accordance with the requirements of the Public and Private Improvement Code. All parking spaces shall be eighteen (18) feet long with a minimum width of ten (10) feet, exclusive of aisle/driveway areas.

G.	Recreation: At least ten percent (10%) of the mobile home park area shall be reserved or dedicated for the recreation purposes of park residents with appropriate location, dimensions and topographic characteristics which, in the judgment of the Township, lend themselves to such recreational uses. This will be a private recreational facility.

H.	Waste Disposal: Dumpsters or other park waste disposal facilities shall be isolated from individual mobile homes by at least fifty (50) feet and shall be screened on at least three (3) sides with a gate on the open side.

I.	Arrangements of Dwelling Units: Modern mobile homes are house-like in appearance and blend more suitably with traditional housing. Because of this, lots for such units will be located on the front and along the side perimeters of mobile home parks. These units are to:

- Be “double wide” [at least twenty-four (24) feet wide].

- Have a sloped roof [a pitch of at least two-and-one-half (2½) feet for each twelve- (12) foot of horizontal run].

J.	Sidewalks: Development of fifty (50) units or more shall provide for sidewalks accessible to all units. Such sidewalks shall be at least four (4) feet wide.

K.	Coverage: Land coverage for individual mobile home lots shall not exceed fifteen percent (15%) for all structures.

Section 706 Utility Requirements

A.	Water and Sewer: All provisions for water and sanitary sewer facilities shall be community systems and not individual on-lot systems. Such systems are to be inspected by the Township and its design shall be as required by DEP and shall be approved by that agency.

B.	Gas, Telephone and Cable: All utility facilities shall be installed and inspected according to the standards set forth by the utility company.

C.	Exterior Lighting: Adequate lights shall be provided to illuminate streets, driveways and walkways for the safe movement of vehicles and pedestrians at night. Full cutoff fixtures shall be as required to minimize glare.

D.	Other Utilities: Shall be underground, as feasible.

Article VIII

Land Development Standards

Section 801 Jurisdiction

In defining the term “land development,” the Pennsylvania Municipalities Planning Code recognizes both subdivisions and other forms of land development. This Article sets forth the standards for these other land developments.

It shall be unlawful for an applicant to construct land developments as defined herein without complying with standards set forth in this Article. Additional criteria for certain land developments are covered in subsequent sections in this Article.

801.1.	Land Development: For the purpose of this Article, the improvement of one (1) lot or two (2) or more contiguous lots, tracts, or parcels of land for any purpose involving a group of two (2) or more residential or nonresidential buildings, whether proposed initially or cumulatively, or a single nonresidential building on a lot or lots regardless of the number of occupants or tenure.

The Pennsylvania Municipalities Planning Code excludes the following developments from being considered as a land development, and, thus, they are not subject to this Article:

A.	The conversion of an existing single-family detached dwelling or single-family semi-detached dwelling into not more than three (3) residential units, unless such units are intended to be a condominium.

B.	The addition of an accessory building, including farm buildings, on a lot or lots subordinate to an existing principal building.

C.	The addition or conversion of buildings or rides within the confines of an enterprise, which would be considered an amusement park. For purposes of this sub-clause, an amusement park is defined as a tract or area used principally as a location for permanent amusement structures or rides. This exclusion shall not apply to newly acquired acreage by an amusement park until initial plans for the expanded area have been approved by proper authorities.

Section 802 Procedures for Land Development (Site Plan)

In lieu of a plot plan, the developer shall submit a site plan. In processing a land development, the three-stage procedure established in this Ordinance for subdivisions shall be used: sketch plan (optional, not mandatory), preliminary site plan, and final site plan. Each land development site plan shall, through one or more pages, show:

A.	Existing site conditions (topography, drainage, tree clusters, buildings, utilities, streets, and neighboring properties).

B.	Proposed developments, including building footprints (with frontal elevation), parking, vehicular and pedestrian access areas, storm drainage, landscaping, utility location and size.

Unless otherwise noted, the processing requirements, drawing size, certifications, acknowledgments, number of copies, etc. for submission of land development site plans shall be the same as for a subdivision, and the final site plan shall be recorded in the Beaver County Recorder’s Office.

Section 803 Final Plan Review

In addition to other final plan requirements for a major subdivision, the following items shall be included for final plan review for all land developments, as applicable:

A.	Site plans, as required in this Article, engineering plans detailing the construction of all required improvements, and other data information establishing compliance with the design standards of this Article.

B.	Proof of approvals by all appropriate public and governmental authorities or agencies where applicable including, but not limited to, permits for any planned road entrances onto existing roads or highways (PennDOT or municipal) and permits or approvals from the Department of Environmental Protection or other State agencies relating to sewage facilities, water obstructions, air quality, etc., as applicable.

C.	In case of multi-owner or multi-tenant developments, proof of the organization and means for management and maintenance of common open space, parking and other common utilities or improvements. Instruments demonstrating creation of an association or entity or other means of assuring continuing maintenance shall be required.

Section 804 Design Standards for Land Developments

Land developments shall meet the following design requirements. It is recognized by the Township of Hanover that the design process should be somewhat flexible, pursuant to the intent of Section 503(5) of the Pennsylvania Municipalities Planning Code.

Generally, the criteria and design for facilities for transportation and parking shall be based upon an accepted professional publications and/or resources.

804.1	General Design

A.	The developer shall make satisfactory provision for the improvements necessary to the proper functioning of the development, including but not limited to, street access signs, water supply facilities, sewage disposal facilities and stormwater management.

B.	The development plan shall provide for adequate privacy, light, air and protection from noise through building design, street layout, screening, plantings, and placement of buildings.

C.	All land developments required to submit plans for approval by the Pennsylvania Department of Labor and Industry shall show evidence of approval by that agency.

D.	Where applicable, proof of a Highway Occupancy Permit (PennDOT) or similar driveway/road access permit shall be required.

804.2	Transportation

A.	Vehicular access connections to the surrounding existing street network shall be safe, shall have adequate sight distances, and shall have the capacity to handle the projected traffic. The developer shall follow the access management standards, as set forth by the Township’s zoning ordinance.

B.	Streets may be planned for dedication to the public or may be planned as private streets to be maintained by the developer or other association or entity. Public streets shall comply with the standards set forth by Articles IV and V of this Ordinance and the Public and Private Improvement Code.  Private streets shall be built to standards appropriate for the traffic load they are to carry.

C.	For multi-building land developments, a complete interior pedestrian circulation plan shall be submitted by all developers indicating the safe and efficient movement of people within and through the site. All traffic, parking, and pedestrian plans shall be completed using such standard resource criteria as provided by the American Planning Association or the Institute of Transportation Engineers (ITE). Copies of any traffic studies required by the Pennsylvania Department of Transportation for road access or signalization will be provided to the Township. That study will be reviewed for completeness using the most current publications of the Institute of Transportation Engineers. If the study does not cover the recommended information of the ITE, supplemental data will be required.

D.	Requirements for Traffic Impact Studies: Any development which is expected to generate a daily traffic volume of three thousand (3,000) trips or more shall prepare a traffic impact study. The study shall follow the recommendations of the Institute of Transportation Engineers (see Transportation and Land Development, latest edition, ITE). See also the Township zoning ordinance.

804.3	Waste Storage and Disposal: Waste storage and disposal areas for the land development shall be planned and constructed in a way that they are shielded from the public right-of-way or neighboring properties. Any “dumpster” shall be in a three-sided structure, enclosed with a gate.

804.4	Parking

A.	A parking and access plan shall be submitted along with estimated traffic flows. The developer shall demonstrate that the proposed parking/access layout is adequate for the proposed development, based upon standard parking capacity measurements, including number of spaces per anticipated development type.

B.	Number of Parking Spaces Required: The number of off-street parking spaces provided shall be based upon standards the Township zoning ordinance.

C.	Drainage and Stormwater Control: All parking and loading areas and access drives shall have either:

- A mud- and dust-free surface, graded with positive drainage, and using pervious material to prevent the flow of surface water onto neighboring properties.

- A paved surface, graded with positive drainage to prevent the flow of surface water onto neighboring properties.

D.	Location and Parking: Required parking spaces shall be located on the same lot with the principal use.

E.	Screening, Landscaping and Setbacks: Off-street parking areas for more than thirty-five (35) vehicles and off-street loading areas shall be effectively screened on any side that adjoins a dwelling, residential district, or platted residential lots. Ten- (10) foot planting strips between the parking lot and all lot lines to be planted with one (1) hardwood or coniferous tree per each twenty (20) parking spaces or combination thereof. Eight percent (8%) of the total interior space shall be devoted to interior planting strips to be maintained in trees, shrubbery, and/or annual plants designed in pervious dust- and mud-free material. Interior planting strips shall be at least eight (8) feet wide unless protected by a bumper block set back two (2) feet from the edge of the planter strip. Drainage plans shall take full advantage of pervious material areas. In addition, there shall be a planting strip of at least eight (8) feet between the front lot line and the parking lot. Such planting strips shall be suitably landscaped and maintained. Any landscaping in the front planting strip shall not include shrubs higher than three (3) feet in height. Trees shall be hardwoods, with at least eight (8) feet of cleared trunk for adequate visibility.

F.	Parking areas in excess of twenty thousand (20,000) square feet shall maintain easements to connect to existing or potential future parking lots on the same or abutting parcels.

804.5	Stormwater Management: A stormwater management plan meeting the requirements of the Township and embracing the principle of no net increase in off-site runoff shall be provided.

804.6	Landscaping: For multi-building land developments, a complete landscaping plan shall be submitted that includes a complete interior landscape plan in addition to a landscaped transition to adjoining properties. Landscape treatment shall be provided to enhance architectural features, manage stormwater runoff or provide energy conservation through climate control.

804.7	Exterior Lighting: Exterior lighting, when used, shall be of a design and size compatible with adjacent areas and in accordance with the standards of the Illuminating Engineer Society. Lighting shall be designed to reduce glare and excessive illumination to surrounding properties while providing for public safety. Full cutoff fixtures will be required.

804.8	Water and Sewer: Water and sanitary sewer service shall be provided in accordance with the standards and requirements of the providing agency.

804.9	Utilities: Gas, electric, telephone, and cable utilities shall be located in land developments in accordance with utility company standards and requirements. All such utilities shall be underground.

Section 805 Assurance for Completion and Maintenance of Improvements

Insofar as the land development involves the lease or rental of buildings and/or space on the site and site improvements (such as streets, parking areas and stormwater drainage devices), which are to be privately maintained or maintained by a private (non-public) organization or entity created by the developer. Where the developer does not intend to maintain the improvement and where a homeowner’s association or similar organization will not be organized for these responsibilities, the developer will submit a plan for maintenance of such facilities. This document will be legally enforceable, one clearly establishing maintenance responsibility. It must be approved by the municipality or any accepting authority.

Section 806 Additional Criteria for Multi-Family Dwellings

806.1	Recreation Area: Multi-family dwellings shall reserve no less than ten percent (10%) of total lot area as passive or active recreation space for the benefit of residents. This land shall be suitable for the purpose for which it is proposed.

806.2	Parking: All required parking shall be on site, with adequate lighting and paved with walkways to the dwelling units.

Article IX

Acceptance of Public Improvements

Section 901 General

Upon completion of street and drainage systems, or any public improvements to be dedicated to the Township, as set forth on the final plan, the developer shall request the Township accept ownership and perpetual maintenance. The Township’s acceptance shall require the following:

901.1	Certificate by the Township Engineer that the improvements have been completed as shown on the final plan and in accordance with the Ordinance.

901.2	Formal acceptance by the Township of the improvements on a form supplied by the Township.

901.3	The Township shall require the posting of financial security for any improvements to be accepted. Said financial security is for the structural integrity and/or functioning of said improvements for a period of eighteen (18) months from the date of their acceptance by the Township and shall be in the amount allowed by Section 509 of the Pennsylvania Municipalities Planning Code, as amended, which is fifteen percent (15%) of the actual cost of installation.

901.4	Submission by the developer of as-built drawings of the said improvements. As-built drawings are to be permanent drawings on stable plastic drafting film and be prepared by a professional engineer or land surveyor. Where the engineer uses a computer-aided drafting system, the Township will request an electronic copy of the subdivision and the public improvements.

901.5	Improvements offered to any municipal Authority shall be subject to their rules and acceptance process. However, proof of acceptance will be required.

Article X

Assurances of Completion

Section 1001 General

The purpose of these regulations is to provide sound subdivision and land development standards for the Township. It is the intention of this Article to provide regulations for public improvements, which are to be dedicated to the Township. Some required improvements may be dedicated to a municipal authority and others to a private utility. The bonding or security in such instances shall comply with that agency’s requirements. As these improvements will be part of the subdivision or land development to be approved, the developer should inform the Township of any problems associated with any provision of bonding or financial security encountered with such agencies.

Section 1002 Improvements

1002.1	The developer shall, for all subdivisions and land developments, agree to complete all improvements in accordance with these regulations or such other improvements as the Township may require in the public interest as a prerequisite to approval of the final plan. Such improvements include those which will be dedicated to the Township, an appropriate municipal authority or similar designated agency.

1002.2	No plan shall receive final plan approval by the Board of Supervisors unless the developer shall have completed all improvements as required by these regulations (see Article IX) or shall have filed with the Township, designated agency or entity surety or other financial security guaranteeing the completion of such improvements.

1002.3	The Board of Supervisors shall require the Township Engineer to check final construction plans for their correctness and to inspect the construction of improvements. The Township Engineer will be used for all improvements where the Township is to assume ownership or be responsible for maintenance. The entire cost of plan review and inspection will be borne by the developer in accordance with the Pennsylvania Municipalities Planning Code [see generally Section 503(1) and 510(g)]. The review and inspection of improvements to be dedicated to designated authorities or agencies where the Township will not maintain same will be in accordance with such organization’s practices.

1002.4	Upon completion of the improvements in accordance with the specifications required by this Ordinance and upon final inspection of the improvements by the Township Engineer, the developer shall take the final steps to make an offer of dedicating the improvements and request the Township to accept same (see Article IX). Improvements to be dedicated to designated authorities or agencies where the Township will not maintain same will be in accordance with such organization’s standards, rules and regulations.

1002.5	Improvements may include, but are not necessarily limited to, the following:

A.	Monuments or markers (see also 603.H).

B.	Grading, streets, curbs and sidewalks, as required.

C.	Sanitary sewers.

D.	Water service, including fire hydrants.

E.	Storm drainage improvements, as required.

F.	Erosion and sedimentation control measures, as required.

G.	Street lighting.

H.	Street signs.

I.	Landscaping

Section 1003 Financial Security

The purpose of this Section is to provide for the filing of financial security as allowed by Section 509 of the Planning Code. Where the improvement is to be dedicated to a designated authority or agency other than the Township, the developer will follow that organization's practices. It is the clear intent of this Ordinance that all improvements required by this Ordinance be either installed and approved, or the developer will post adequate financial security as required by Section 509 of the Planning Code before final plan approval is granted.

1003.1	An assurance of proper completion of the improvements by financial security in the subdivision shall be made by one of the following methods, or such other method as shall be satisfactory to the Township:

A.	A bond, irrevocable letter of credit, restrictive or escrow account, certified check, or other security satisfactory to the Township and in accordance with Section 509 of the Planning Code, which shall run or be made payable to the Township.

B.	In the case of a bond, it shall also:

- Be with surety satisfaction to the Township.

- Be in form, sufficiency, and execution acceptable to the Township.

1003.2	The amount of the financial security shall be in an amount determined to equal one hundred ten percent (110%) of the cost of the required improvements in accordance with Section 509 of the Planning Code, and shall be approved by the Township Engineer.

1003.3	The bond, certified check or other securities shall specify the time for the completion of the required improvements. Such time shall be satisfactory to the Board of Supervisors, but not exceed one (1) year. When the improvements have been completed and approved by the Township, the guarantee shall be released and returned. When a portion of the required improvements has been completed and approved by the Township, a portion of the bond, monies or security commensurate with the cost of the improvement may be released and returned in accordance with Section 509 of the Planning Code.

In no event shall the entire performance assurance be returned to the developer. At least fifteen percent (15%) shall be retained until:

A.	All improvements have been completed, approved by the Township Engineer and accepted by the Township of Hanover.

B.	The required bond for structural integrity/functioning (see Article IX) has been filed and accepted by the Township.

C.	All the requirements of Article IX, specifically including the filing of as-built drawings, have been met.

1003.4	In the event that cash or its equivalent is deposited as an improvement guarantee, it shall be held in an escrow fund, which may bear interest to the credit of the developer, but the developer shall pay all costs for the maintaining of such escrow fund.

1003.5	As the work of installing the required improvements proceeds, the developer posting the financial security may request the Board of Supervisors to release of such portions of the financial security necessary for payment to the contractor or contractors performing the work. Any such requests shall be in writing, addressed to the Board of Supervisors, and the Board of Supervisors shall have forty-five (45) days from receipt of such request within which to allow the Township Engineer to certify, in writing, that such portion of the work on the improvements has been completed in accordance with the approved plan and specifications. On such certification, the Board of Supervisors shall authorize release by the bonding company or lending institution of an amount as estimated by the Township fairly representing the value of the improvements completed or, if the Board of Supervisors fails to act within said forty-five (45) day period, the Board of Supervisors shall be deemed to have approved the release of funds as requested.

1003.6	For circumstances relating to financial security not specifically delineated in the Ordinance, including the amount of same and the resolution of disagreements relative to such security, it is the intention of the Township to follow the guidelines and procedures as set forth by Sections 509 and 510 of the Pennsylvania Municipalities Planning Code.

1003.7	In the event that any improvement which may be required have not been installed as provided in the Ordinance or in accordance with the approved final plan, the Township may enforce any corporate bond, or other security by appropriate legal and equitable remedies. If proceeds of such bond, or other security, are insufficient to pay the cost of installing or making repairs or corrections to all the improvements covered by said security, the Township may institute appropriate legal or equitable action to recover the monies necessary to complete the remainder of the improvements. All of the proceeds shall be used solely for the installation of the improvements covered by such security, and not for any other Township purpose.

Article XI

Administration, Amendment, and Modification

Section 1101 Amendments

The Board of Supervisors of the Township of Hanover may, from time to time revise, modify, and amend this Ordinance by appropriate action in accordance with the Pennsylvania Municipalities Planning Code, Act 247, as amended.

Section 1102 Filing Fee and Review

The filing fee for subdivision plans shall be established by the Board of Supervisors. Such filing fees shall include those for mobile home parks and land development. Fees shall include the review of subdivision plats, mobile home park plans, and land development site plans and this recordation. Fees shall also include the field inspection of such plats, plans, or site plans or their final inspection. The fees charged to the developer shall be in accordance with 503(1), 509, and 510 of the Pennsylvania Municipalities Planning Code.

Section 1103 Records

The Township shall maintain an accurate public record of all plans upon which it takes action and of its findings, decisions, and recommendations in relation thereto.

Section 1104 Appeals

In any case where the Board of Supervisors approves or disapproves a subdivision or land development plan, any person aggrieved thereby may, within thirty (30) days thereafter, appeal to the Court of Common Pleas of Beaver County, Pennsylvania in accordance with Article X-A of the Pennsylvania Planning Code.

Section 1105 Validity

Should any section or provision of this Ordinance be declared by a court of competent jurisdiction to be invalid, such decision shall not affect the validity of the remainder of this Ordinance as a whole, or any individual part thereof.

Section 1106 Remedies and Enforcement

1106.1 Preventive Remedies

A.	In addition to other remedies, the Township may institute and maintain appropriate actions by law or in equity to restrain, correct or abate violations, to prevent unlawful construction, to recover damages and to prevent illegal occupancy of a building, structure, or premises. The description by metes and bounds in the instrument of transfer or other documents used in the process of selling or transferring shall not exempt the seller or transferor from such penalties or from the remedies herein provided.

B.	The Township may refuse to issue any permit or grant any approval necessary to further improve or develop any real property which has been developed or which has resulted from a subdivision of real property in violation of this Ordinance or preceding regulations of the Township. This authority to deny such a permit or approval shall apply to any of the following applicants:

- The owner of record at the time of such violation.

- The vendee or lessee of the owner of record at the time of such violation without regard as to whether such vendee or lessee had actual or constructive knowledge of the violation.

- The current owner of record who acquired the property subsequent to the time of violation without regard as to whether such current owner had actual or constructive knowledge of the violation.

- The vendee or lessee of the current owner of record who acquired the property subsequent to the time of violation without regard as to whether such vendee or lessee had actual or constructive knowledge of the violation.

As an additional condition for issuance of a permit or the granting of an approval to any such owner, current owner, vendee or lessee for the development of any such real property, the Township may require compliance with the condition that would have been applicable to the property at the time the applicant acquired an interest in such real property.

1106.2 Enforcement Remedies

A.	Any person, partnership or corporation who or which has violated the provisions of this Subdivision or Land Development Ordinance enacted under the Pennsylvania Municipalities Planning Code or prior enabling laws shall, upon being found liable therefore in a civil enforcement proceeding commenced by the Township, pay a judgment of not more than five hundred dollars ($500), plus all court costs, including reasonable attorney fees incurred by the Township as a result thereof. No judgment shall commence or be imposed, levied or be payable until the date of the determination of a violation by the district justice. If the defendant neither pays nor timely appeals the judgment, the Township may enforce the judgment pursuant to the applicable rules of civil procedure. Each day that a violation continues shall constitute a separate violation, unless the district justice determining that there has been a violation further determines that there was a good faith basis for the person, partnership or corporation violating the ordinance to have believed that there was no such violation, in which event there shall be deemed to have been only one such violation until the fifth (5th) day following the date of the determination of a violation by the district justice and thereafter each day that a violation continues shall constitute a separate violation.

B.	The Court of Common Pleas, upon petition, may grant an order of stay, upon cause shown, tolling the per diem judgment pending a final adjudication of the violation and judgment.

C.	Nothing contained in this section shall be construed or interpreted to grant to any person or entity other than the Township the right to commence any action for enforcement pursuant to this section.

Section 1107 Modification of Regulations

1107.1	The Board of Supervisors may grant a modification of the requirements of one (1) or more provisions of this Ordinance if the literal enforcement will exact undue hardship because of peculiar conditions pertaining to the land in question, provided that such modification will not be contrary to the public interest and that the purpose and intent of this Ordinance is observed. The Supervisors shall use the following guidelines in considering requests for modifications:

A.	There is a unique physical characteristic of the development which requires the modification. This characteristic shall be isolated to development in question.

B.	That the modification is not issued for reasons of economic hardship.

1107.2	All requests for a modification shall be in writing and shall accompany and be a part of the application for development. The request shall state in full the grounds and facts of unreasonableness or hardship on which the request is based, the provision or provisions of the ordinance involved and the minimum modification necessary. The Planning Commission‘s advice on any modification will be requested before the Board of Supervisors takes action on such requests.

1107.3	The Board of Supervisor shall keep a written record of all action on all requests for modifications.

1107.4	The Board of Supervisors may approve, or deny the request for modification. If the Board of Supervisors approves the request for modification, it shall authorize the minimum modification from this Ordinance that will afford relief.

Section 1108 Conflict

Whenever there is a difference between the minimum standards or dimensions specified herein and those contained in other regulations, resolutions, or ordinances of the Township, the highest standards shall govern.

# Footnotes

Richard D. Schein. 1993. Tree Works